## Slide 1: Meat Packaging
ANSC 3404

## Slide 2: Purpose of food packaging
Protect products
Contain the product
Communicate to the consumer as a marketing tool
Provide consumers with ease of use and convenience

## Slide 3: Why is Packaging Important?
Appearance (color) greatest influence on consumer purchase
Food package protects against deteriorative effects
Ideally, packaging should promote or enhance shelf-life

## Slide 4: Shelf-life
Factors that determine shelf-life
  Water holding capacity
  Color
  Microbial load
  Lipid stability
Utilization of correct package can extend shelf life

## Slide 5
50 years ago & before: Butcher shops and full-service meat markets
  Family owned and operated butcher shops
  Meat wrapped in butcher paper and sold on demand basis

## Slide 6: 1950’s-present: Refrigerated Self-Service Display Cases
Increased consumer demand for convenience
  Conversion to a 24-hour day stores
  Ability to buy meat at all times
  Increased requirements for food safety and wholesomeness
  Competition in the market place

## Slide 7: Historical Changes in Packaging
Meat cut and packaged by consumer
  Animals harvested as needed
Meat cut by butcher and wrapped in wax paper
1950’s: Increased use of overwrap packaging
  1950’s-1990’s: Advances in packaging technology
  Increased user of barrier packaging (PVC)
  Vacuum packaging
1990’s-current: Implementation of New Technology
  Need for Case-Ready Products
MAP, Skin-pack, Darfresh, etc

## Slide 8: Myoglobin

## Slide 9: Vacuum Packaging
Utilized in Plants for Boxed Beef
Oxygen impermeable
  Formation of Deoxymyoglobin
Moisture Impermeable
Extends Shelf Life
  Requires strict temperature
  for control of anaerobic microorganisms
Current equipment used:
  Multi-chamber, heat sealing 30+pieces per minute
Disadvantages
  Consumer acceptability of
  Deoxymyoglobin color
  Lack of Bloom

## Slide 11: Traditional Overwrap Packaging
  Uses styrofoam trays
  Uses Polyvinyl Chloride (PVC) wrap
  Moisture impermeable
  Permeable to Oxygen:
    Allows for bright red color because oxygen can be transmitted across

## Slide 12: Traditional Overwrap Packaging
  Advantages of Overwrap
    Increased marketability
    Attractive appearance
Disadvantages:Leaky, messy packages
  Shorter shelf-life
  Exposure to O2
    aerobic bacterial growth
    lipid and pigment oxidation

## Slide 13: Modified Atmosphere Packaging
“MAP is the removal or replacement of the atmosphere surround the product before sealing in vapor-barrier materials”(McMillin, Huang, Ho, & Smith, 1999)
Types of MAP
  Vacuum
  Oxygen/CO2,Nitrogen
  High Oxygen/ Low Oxygen
  Carbon Monoxide
  Peelable Films
  Master Bag

## Slide 14: Types of MAP
High-Oxygen MAP80% O2/ 20% CO2
  is most common
  Exposure to high oxygen atmosphere increases presence of oxymyoglobin
  Decreased shelf-life
    Aerobic bacterial growth
    Lipid and pigment Oxidation
  Increased Oxidation
    Decreased flavor
    Increased off-odors
    Increased discoloration
    Growth of spoilage microorganisms

## Slide 15: Types of MAP
Low Oxygen MAP
  Includes skin-packaging and vacuum
  Absence of Oxygen in Low-Ox MAP
    causes formation of DMb
  Commonly used for “Master Packing” of Overwrap packages
    Non-barrier overwrap packages enclosed in Low-Ox master pack
    When removed from Master Pack and exposed to O2 bloom occurs
Decreased lipid and pigment oxidation
  Promotes shelf life
Decreased microbial growth
Problems with consumer acceptability of DMb color

## Slide 16: Types of MAP
Low Oxygen MAP
  One type of Low-Ox MAP alleviates DMb color problem
    CO-MAP
Carbon monoxide achieved GRAS status from FDA in 2002.
  Approved for use at 0.4%
Benefits of CO-MAP
  Increased control of oxidation
  Formation of stable red color due to Carboxymyoglobin
  Superior flavor by reduced lipid oxidation
  Decreased discoloration by decreased MMb formation

## Slide 17: Comparison of Low-Ox vs. High-Ox Packaging

## Slide 18: SSD/ SES
Used in the Poultry industry

## Slide 19: Darfresh

## Slide 20
Laminate
  Provides nice view of product
Chubs

## Slide 21: Poultry Shrink Bag

## Slide 22: Simple Steps
Convenience
Value added

## Slide 23: Packaging Systems

## Slide 24: Major Packaging Change
Change from passive to active packaging
Food packaging originated as a means for protecting the properties of the product, but has evolved to provide and enhance many functions for the product itself.

## Slide 25: Summary
Modern packaging technology and equipment provide the industry with the means to modify and enhance product quality and shelf life
Requires understanding of quality and shelf-life factors and utilization of packaging technology to correct downfalls and capitalize on advantages.

## Slide 26: Future
Further extension of shelf-life
  Addition of antioxidants or antimicrobials
  New packaging systems and types