## Slide 1: Lab safety
Note for lab safety training/talk on Nov.20, 2011
Environmental Health & Safety website: http://www.depts.ttu.edu/ehs/Web/

## Slide 2: Required documents
SOPs for anything potentially dangerous
  Including how to change MOCVD bubbler, dump sharp/chemical waste, use fume hood
Lab safety plan – must have, in written form
  Approved by PI
  Risk analysis from EHS (optional)
  eg. annual inspection, training
MSDS
  Storage(flammable/reactive)
  Shipping requirements

## Slide 3: Training
Location of first-aid, fire extinguishers and spill kits
Personal Protective Equipments (PPE)
  Gloves: one time use, take off inside-out and dump in regular trash
  Body cover: no exposed skin from waist down
  Shoes: full foot coverage, no cloth or absorbent materials
  Eyewear, respirator/ventilation
Waste management
  Waste chemicals: separately stored in labeled containers mark with full name and date.
  Waste sharp items: special container or sharp edge secured
Notes: Respirator: only use when necessary, (try ventilation first) – Must have annual “fitting test”

## Slide 4: Training
Chemical Hygiene
  Designated area - fume hood: sash below mark
  Separate flammable/reactive/waste inside fume hood
  Glassware: rinse after use, label if left in fume hood
  Store chemicals accordingly
    Separate flammable/inflammable, base / acid, HF
    Specialized cabinet / refrigerator (EHS can provide)
  Handle spills: call (2-3876) immediately if unsure
    Use spill kits if comfortable
  HF: especially dangerous, penetrate gloves in seconds.
Notes: Spills: MUST call if mercury. Care if deal with self about carcinogen, mutagen, reactive,